## Slide 1
Symptom:white screen when turning ON
Check the connection of the motherboard
 Reconnect it
Check the video output of the motherboard
replace mother board (see page 32 of E100M011 technical manual or movie 6)
Check the connector HE15 zone PC of the power supply
 Reconnect it or change power module (see page 48 of E100M011 manual)
unsolved
unsolved
solved
ACTIONS